Note: This IBM PC BIOS API call is for DOS/Win16 personality only. Use Family API for portability.
Note: osFree Macro Library provides macros for most of functions
# @AuxInit
## Brief
Initialize serial port
## BIOS Interrupt
INTH: H
## Family API
fapi
## Syntax
@AuxInit port, settings

## Parameters
- port (WORD) - port number
- settings (BYTE) - port settings
Baud rates is passed in the high order 3 bits as follows:
000	110 baud
001	150 baud
010	300 baud
011	600 baud
100	1200 baud
101	2400 baud
110	4800 baud
111	9600 baud

Bits 4-3 define parity:
00	no parity
10	no parity
01	odd parity
11	even parity

Bit 2 defines stop bits:
0	1 stop bit
1	2 stop bits

Bits 1-0 character length:
10	7 bits
11	8 bits

## Return
AX - port status
Bitfields for serial line status (AH):
Bit(s)	Description
7	timeout
6	transmit shift register empty
5	transmit holding register empty
4	break detected
3	framing error
2	parity error
1	overrun error
0	receive data ready

Bitfields for modem status (AL):
Bit(s)	Description
7	carrier detect
6	ring indicator
5	data set ready
4	clear to send
3	delta carrier detect
2	trailing edge of ring indicator
1	delta data set ready
0	delta clear to send