### KbdGetCp
Bindings: C, MASM
This call allows a process to query the code page being used to translate scan codes to ASCII characters.
KbdGetCp (Reserved, CodePageID, KbdHandle)
Reserved (ULONG) - input Reserved and must be set to zero.
CodePageID (PUSHORT) - output Address of the code page ID located in the application's data area. The keyboard support copies the current code page ID for a specified keyboard handle into this word. The code page ID is equivalent to one of the code page IDs specified in the CONFIG.SYS CODEPAGE = statement or 0000.
KbdHandle (HKBD) - input Default keyboard or the logical keyboard.
rc (USHORT) - return Return code descriptions are:
0	NO_ERROR
373	ERROR_KBD_PARAMETER
439	ERROR_KBD_INVALID_HANDLE
445	ERROR_KBD_FOCUS_REQUIRED
447	ERROR_KBD_KEYBOARD_BUSY
464	ERROR_KBD_DETACHED
504	ERROR_KBD_EXTENDED_SG

Remarks
The CodePageID is the currently active keyboard code page. A value of 0 indicates the code page translation table in use is the ROM code page translation table provided by the hardware.
#### C bindings
#define INCL_KBD USHORT rc = KbdGetCp(Reserved, CodePageID, KbdHandle); ULONG Reserved; /* Reserved (must be zero) */ PUSHORT CodePageID; /* Code Page ID */ HKBD KbdHandle; /* Keyboard handle */ USHORT rc; /* return code */

#### MASM bindings
EXTRN KbdGetCp:FAR INCL_KBD EQU 1 PUSH DWORD Reserved ;Reserved (must be zero) PUSH@ WORD CodePageID ;Code Page ID PUSH WORD KbdHandle ;Keyboard handle CALL KbdGetCp Returns WORD